## Slide 1: Loyola MARS inert gas system simulator
Programmed and Designed by Harrison Leece
Presentation by Harrison Leece

## Slide 2
Helium or N2
Liquid Oxygen
Kerosene
Gas ullage and propellants
Pressure Regulator
Model overview:

## Slide 3: Assumptions
Adiabatic
Reversible
No pressure losses from regulator to tanks

## Slide 4
Helium or N2
Liquid Oxygen
Kerosene
Table look-up from P_0 and T_0
Desired Ullage pressure = 400-450 psia CONSTANT
Heating or Cooling over Throttle
Adiabatic expansion from P_0 and T_0 to P_t and T_t at any discrete time ‘t’ at step ‘n’
Method 1: Isentropic Expansion Eqns
Because is a function of T and , the average gamma of every time step is used as the ‘instantaneous’

## Slide 5: A quick hand-calc for this method
Fluid species = Helium
2,930,000 Pa= 425psia
34470000 Pa = 5000 psia
h = .001 seconds/step
Mass flow/step = .00002 kg/step
Initial density = 1.442kg/.03m^3 = 48.067 kg/m^3
= ~1.6
10.2977 kg/m^3
(1.442 - .309) / (Mass flow / step ) = #steps = 56650 steps
56650 steps * .001 seconds/step = 56.65seconds predicted

## Slide 6: Unit testing, Method 1: Supply tank with constant mass flow rate
Decouples the unknown of required mass flow rate to test constant volume supply tank
Concave up pressure
Concave down temperature
Initial tank conditions: V = .03 m^3, P = 34470000Pa, 1.442 kg
Gas species = Helium
Per step:
Step size: h = .001 sec
Simulation ends when P<2930000Pa
56.2 seconds Nice!
Mass vs time

## Slide 7
Helium or N2
Liquid Oxygen
Kerosene
Table look-up from P_0 and T_0
Desired Ullage pressure = 400-450 psia CONSTANT
Heating or Cooling over Throttle
Differentiate adiabatic expansion equations:
Method 2: Derivative of Isentropic Eqns
With respect to rho:
Now substitute all terms to be , valid for infinitesimal rho steps (I claim).
Calculate as a function of T and at each step with a table look-up
Apply Euler’s Method (can be improved with Heun’s or RK4 methods )
=
=

## Slide 8: Unit testing, Method 2: Supply tank with constant mass flow rate
Decouples the unknown of required mass flow rate to test constant volume supply tank
Concave up pressure
Concave down temperature
Initial tank conditions: V = .03 m^3, P = 34470000Pa, 1.442 kg
Gas species = Helium
Per step:
Step size: h = .001 sec
Simulation ends when P<2930000Pa
55.9 s
Mass vs time

## Slide 9
Helium or N2
Liquid Oxygen
Kerosene
Table look-up from P_0 and T_0
table look-up with 0K reference
Desired Ullage pressure = 400-450 psia CONSTANT
Heating or Cooling over Throttle
Method 3: Second Law of Thermodynamics for Open Systems
table look-up with and
Assume Adiabatic and Reversible:
Apply Euler’s Method (can be improved with Heun’s or RK4 methods)
table look-up with and
table look-up with and

## Slide 10: Unit testing, Method 3: Supply tank with constant mass flow rate
Decouples the unknown of required mass flow rate to test constant volume supply tank
Concave up pressure
Concave up temperature
Temperature approaches 50K!
½ the time of method 1 and 2
Initial tank conditions: V = .03 m^3, P = 34470000Pa, 1.442 kg
Gas species = Helium
Per step:
Step size: h = .001 sec
Simulation ends when P<2930000Pa
Mass vs time
~28 seconds ?

## Slide 11
Helium or N2
Liquid Oxygen
Kerosene
Desired Ullage pressure = 400-450 psia CONSTANT
Table lookup specific enthalpy from P_t and T_t
before throttle
Table lookup exit temperature from and

## Slide 12
Propellant to Engine with known mass-flow rate kg/s
Pressurizing gas flowing into engine with known temperature and pressure
Objective: Maintain desired pressure in the ullage of the tank
Mass-flow rate must be found to sustain desired pressure
Once mass-flow rate is known, a new ullage temperature can be found using the equation:
Find this volume delta based on propellant mass-flow rate divided by propellant density
Units are in meters^3/sec
can then be multiplied by a small time step to get a very small volume in m^3 units
Mass-flow from upstream must be enough to maintain the density of the inert-gas in the ullage, BUT the properties of entering gas and ullage gas are not identical….

## Slide 13: Density convergence algorithm
Simulation step size
J-T effect supply temperature
Once algorithm succeeds, update tank state and add added mass to plotting list for debugging
Table look-up in cython
Seek convergence

## Slide 14: Plots
Supply tank
Propellant tanks
Mass of He required: 1.45 kg
Volume of supply tank: .03m^3 or ~8 US gallons
Pressure of supply tank: 5000 psia

## Slide 15: What we can find from this
MINIMUM inert gas mass required per firing
Temperature ranges for components
Inert gas tank volume and pressure requirement MINIMUMS

## Slide 16: Feedback
If anything looks suspicious in the methodology, PLEASE email me at hleece@lion.lmu.edu or text me at (669) 258-1729